## Slide 1
Airbus Defence and Space SAS Proprietary and Confidential
Domino-X: Dominoes’ cardinality
DOMX-TN-ADST-1001591482
16/02/2023
Nicolas MAYER

## Slide 2
Domino-X Ground Segment
Domino’s perimeter
A domino could be multi-mission,
or dedicated to one mission
Domino’s unicity constraint
A domino could be unique (central), by design
Or many concurrent implementation can be deployed
Optionality
A domino could integrates mandatory features,
Or optional features
Scope
Multi-mission
Dedicated to one mission
Unicity constraint
Shall be unique (central)
Could be many
Optionality
Mandatory
Optional

## Slide 3
Domino-X Ground Segment
Domino’s scope: Payload dependency
A domino could be multi-mission,
or dedicated to one mission
Programing Request Service
  [PRS] domino is very close to the mission capabilities, and knows the mission particularities
Mission Programming Service
  [MPS] domino is linked with the mission capabilities and particularities, and knows the details of the payload control
Pivot Processing Service
VHR
Pivot Processing Service
HR
Mission Services
Image Quality
Service
« Machine-learning Application » Production & Quality
Service [MAPQS]
VHR
HR
2x VHR satellites
Platform
Payload
8x HR satellites
Platform
Payload
Pivot Processing Service
  [PPS] domino knows the instrument particularities and knows how to decipher and decompress the ITM. It also knows how to build a “perfect sensor” product, without these particularities
Image Quality Service
  [IQS] domino is focused on the instrument characteristics needed to calibrate it (on ground or in-board)
Processing Services
Mission Programming Service
VHR
Mission Programming Service
HR

## Slide 4
Domino-X Ground Segment
Domino’s perimeter: Platform dependency
A domino could be multi-mission,
or dedicated to one mission
Mission Planning Service
  [MPS] domino knows the platform characteristics, and computes the satellite’s manoeuver between acquisitions
TM/TC Ciphering Service
  [TTCS] domino is linked with the on-board ciphering/deciphering equipment and its capabilities
Flight Operation Service
  [FOS] domino is linked with the spacecraft platform characteristics
Flight Dynamics Service
  [FDS] is linked with the spacecraft platform characteristics
Satellite Simulator Service
  [SSS] domino simulates the behaviour of the spacecraft platform (and the payload control)
2x VHR satellites
Platform
Payload
8x HR satellites
Platform
Payload
Satellite Simulator Service
Satellite Simulator Service
Flight Operation Service
VHR
Flight Operation Service
HR
VHR
HR
TM/TC Ciphering Service
TM/TC Ciphering Service
VHR
HR
SCC
Flight Dynamics Service
HR
Flight Dynamics Service
VHR
Mission Programming Service
Mission Programming Service
VHR
HR

## Slide 5
Domino-X Ground Segment
Domino’s unicity constraint
A domino could be unique, by design
Or many concurrent implementation can be deployed
Dominoes unique by design (multi mission)
  Knowledge Builder and Decision Service
  Federation Service
  User Access Service
  Operational Monitoring Service
  E2E Performance Monitoring Service
  Security Monitoring Service
  Archive/Catalogue Service
  Data Integrity & Tracability Service
  System Configuration Management Service
  Auxiliary Data Gathering Service
  Data Distribution
  Satellite Communication & Resource Mgmt Service
A single instance deployed across the entire ground segment. This instance can manage HR and VHR
Dominoes unique by design (mono mission)
  Mission Programming Service
  TM/TC Cyphering Service
  Satellite Simulator Service
  Flight Dynamic Service
  Flight Operation Service
  Pivot Processing Service
  Image Quality Service
Only one instance deployed per mission. This means one instance for the HR mission and another for the VHR mission
Dominoes with concurrent implementations possibly deployed
  Interoperability Service
  Advanced Processing Service
  Enhanced Processing Service
  Analytic Quality Service
Multiple instances can be deployed. Each of them extends the capabilities of the ground segment (without dependency with the other ones)

## Slide 6
Domino-X Ground Segment
Optionality
A domino could integrate mandatory features
Or optional features
Advanced Processing Service
  In case [APS] domino is missing, the Ground Segment will not be able to process image with processing level greater than pivot level (Perfect sensor), without other major impact
Enhanced Processing Service (and its Quality Service)
  In case [EPS] domino is missing, the Ground Segment will not be able to use image extraction algorithms, without other major impact
Advanced Processing
Service
Enhanced Processing
Service
Knowledge Builder & Decision Service
  In case [KBDS] domino is missing, the Ground Segment will loose its ability to follow-up an event (detect/react/synthetize) and to enhance the image product (metadata), without other major impact
Data Integrity and Traceability Service
  In case [DITS] domino is missing, the Ground Segment will not be able to check the products integrity, and to provide their traceability
Knowledge Builder & Decision Service
Data Integrity & Tracability Service
Minor impacts, to avoid by design:
Monitoring services with [TMS], [EPMS], [SMS]
  They should consider the presence/lack of the optional dominoes by configuration
  End-user visibility [ACS], [UAS], [FS]
  The missing capabilities should not be presented to the end-user (“get capabilities” features)
Analytics Quality
Service

## Slide 7
Multi-Mission User Services
2x VHR satellites
8x HR satellites
Ext. data
Owned GS
Domino-X Ground Segment
Targeted deployment
One “VHR” 2 sat constellation
One “HR” 8 sat constellation
Monitoring Services
SCC
Mission Services
Ressource Management
GSaaS
Processing Services
Data Management Services
Ext. provider
End user
Operators

## Slide 8
Domino’s mode
= “as a service” mode in targeted deployment (operated by an industrial)
2x VHR satellites
8x HR satellites
Satellite Communication & Resource Mgmt Service
GSaaS
Knowledge Builder & Decision Service
Archive/Catalogue Service
Multi
Satellite Simulator Service
Satellite Simulator Service
Mission Programming Service
VHR
Mission Programming Service
HR
Flight Operation Service
VHR
Flight Operation Service
HR
Flight Dynamics Service
VHR
HR
Pivot Processing Service
VHR
Pivot Processing Service
HR
TM/TC Ciphering Service
TM/TC Ciphering Service
VHR
HR
Mission Services
SCC
Ressource Management
Advanced Processing
Service
Enhanced Processing
Service
Multi
Multi
Image Quality
Service
« Machine-learning Application » Production & Quality
Service [MAPQS]
Image Quality
Service
VHR
HR
Multi
Processing Services
Auxiliary Data Gathering Service
System Configuration Management Service
Data Integrity & Tracability Service
Data Distribution
Federation
Service
Interoperability Service
User Access
Service
1
Multi
Multi
Multi-mission User Services
Ext. data
Data Management Services
Operational Monitoring
Service
Security Monitoring
Service
Monitoring Services
Multi
Multi
Multi
Multi
Multi
Multi
Multi
Multi
Owned GS
Ext. provider
End user
Domino-X Ground Segment
Targeted deployment
One “VHR” 2 sat constellation
One “HR” 8 sat constellation
Domino’s perimeter
= dedicated to an homogenous constellation
= multi-mission
= external system
VHR
HR
Multi
Domino’s instances
= one unique instance of this domino
= could be many instances deployed
Without “redundancy” dimension
1
n
Operators
aaS
aaS
aaS
aaS
1
1
1
1
1
1
1
1
1
1
1
1
1
n
1
n
1
n
Operated by the domino’s providers
Maintenance contracts (L3)
1
1
1
1
1
1
HR
Flight Dynamics Service
1
VHR
1
1
?
Domino’s optionality
= The dominoes’ functionalities are not mandatory, depending on the needs
1
EXT
EXT
16/02/2023

## Slide 9: Domino-X Ground Segment overview > Focus on Federation chain
Central role of the [Federation Service]
User requests management
Services discovering of other dominoes
Organisation of production workflows
Local and external systems optimisation
Notes: La Fédération aura un rôle d’organisation de workflows (ordre d’exécution vers les autres dominos), issus des découvertes de service.

## Slide 10: Domino-X Ground Segment overview > Focus on Mission & Control chains
Control chain could be quite “sensible”, particularly the Satellite simulator and TM/TC keys

## Slide 11: Domino-X Ground Segment overview > Focus on Image chain
Industrial breakdown of the Image chain:
The [Pivot Processing Service] dominoes are dedicated to one mission (homogeneous constellation)
The [Advanced Processing Service] and [Enhanced Processing Service] are multi-mission
The [Image Quality Service] (calibration) and [Machine-learning Application Production & Quality Service] (MLOPS) is mainly foreseen “as a service”.

## Slide 12: Domino-X Ground Segment overview > Focus on Data Management > Focus on Monitoring